## Slide 1: Introduction to SDF

## Slide 2: SDF- Simulation Description Format
  SDF is an XML format used to describe objects and environments for robotics simulation.
  SDF Models can range from simple shapes to complex robots.
  It refers to the <model> SDF tag, and is essentially a collection of links, joints, collision objects, visuals, and plugins.
  Generating a model file can be difficult depending on the complexity of the desired model..
  Facilitates accurate modeling of robots, sensors, and environments in simulation platforms like Gazebo.
Comparison with URDF:
  URDF focuses on robot kinematics; SDF encompasses both kinematics and dynamics.

## Slide 3: Components of SDF Models
Links: A link contains the physical properties of one body of the model. This can be a wheel, or a link in a joint chain. Each link may contain many collision and visual elements. Try to reduce the number of links in your models in order to improve performance and stability.
For example, a table model could consist of 5 links (4 for the legs and 1 for the top) connected via joints. However, this is overly complex, especially since the joints will never move. Instead, create the table with 1 link and 5 collision elements.
Collision: A collision element encapsulates a geometry that is used for collision checking. This can be a simple shape (which is preferred), or a triangle mesh (which consumes greater resources). A link may contain many collision elements.
Visual: A visual element is used to visualize parts of a link. A link may contain 0 or more visual elements.
Inertial: The inertial element describes the dynamic properties of the link, such as mass and rotational inertia matrix.
Sensor: A sensor collects data from the world for use in plugins. A link may contain 0 or more sensors.
Light: A light element describes a light source attached to a link. A link may contain 0 or more lights.
Joints: A joint connects two links. A parent and child relationship is established along with other parameters such as axis of rotation, and joint limits.
Plugins: A plugin is a shared library created by a third party to control a model.

## Slide 4: Structure of SDFOverview:
Every SDF file begins with a <sdf> element.
Key Components:
<model>: Represents the robot or object.
<link>: Defines parts of the model.
<joint>: Connects links together.

## Slide 5
Model:Defines a model's properties (e.g., name, static).
Eg:
<model name="example_robot">
<static>false</static>
</model>

## Slide 6
Link:Each link can have visual, collision, and inertial properties.
Joint:Types include revolute, prismatic, etc.
Eg:
<joint name="joint_name" type="revolute">
<parent>link1</parent>
<child>link2</child>
</joint>

## Slide 7: Geometry and Materials
Geometries:Common shapes: box, cylinder, sphere, and mesh.
Materials:Define color and texture.
Eg:
  <material>
  <script>
  <uri>file://media/materials/scripts/gazebo.material</uri>
  <name>Red</name>
  </script>
  </material>

## Slide 8: Pose and Orientation
Pose specifies the position and orientation of links and joints.
Components:
  Position: x, y, z
  Orientation: roll, pitch, yaw
  Eg
  <pose>0 0 0 0 0 0</pose>

## Slide 9: Physical Properties
Accurate mass and inertia are crucial for realistic simulation.
  <inertial>
  <mass>1.0</mass>
  <inertia>
  <ixx>0.01</ixx>
  <iyy>0.01</iyy>
  <izz>0.01</izz>
  </inertia>
  </inertial>