## Slide 1: Introduction to Robot Simulation (Gazebo)

## Slide 2
Gazebo is a free, open-source robot simulation environment.
The project is run by Open Robotics, the same group looking after ROS, however the projects are managed separately and Gazebo is not a "part of" ROS.
This distinction can sometimes be a little confusing, and although Gazebo and ROS do integrate very well, they approach some things a bit differently.
With Gazebo,can create a virtual "world", and load simulated versions of our robots into it. Simulated sensors can detect the environment, and publish the data to the same ROS topics that real sensors would, allowing easy testing of algorithms.
Then, forces can be applied to the simulated actuators on the robot, taking into account things like friction.

## Slide 3: Defining the Structure
Each “Link” is a reference frame of a sensor
Each “joint” defines the transformation that maps the child link in the parent link.
ROS does not handle closed kinematic chains, thus only a “tree” structure is allowed
The root of the tree is usually some convenient point on the mobile base (or on its footprint)
Slide Credit: Wolfram Burgard, University of Freiburg

## Slide 4: Robot Simulation
Simulators mimic the real world, to a certain extent
Simulates robots, sensors, and objects in a 3-D dynamic environment
Generates realistic sensor feedback and physical interactions between objects
Why use them?
Save time and your sanity
Experimentation much less destructive
Use hardware you don’t have
Create really cool videos
Plugins Sensors Models Worlds
Physics
ODE
Bullet
Actuators Sensors
Embedded controllers
Tools Rviz CLT
Nodes Controller Planner
Communications
Topics Services
HARDWARE

## Slide 5: Simulation Architecture
Client
(your program)
Player
Gazebo
Stage
Real Hardware
Cmd
Data
TCP/IP
TCP/IP
TCP/IP
SHM

## Slide 6: Simulation Architecture
Gazebo runs two processes:
Server: Runs the physics loop and generates sensor data.
  Executable: gzserver
  Libraries: Physics, Sensors, Rendering, Transport
Client: Provides user interaction and visualization of a simulation.
  Executable: gzclient
  Libraries: Transport, Rendering, GUI
$ gzserver
$ gzclient
Run Gazebo server and client separately:
$ gazebo
Run Gazebo server and client simultaneously:

## Slide 7: Elements within Simulation
World
  Collection of models, lights,plugins and global properties
Models
  Collection of links, joints,sensors, and plugins
Links
  Collection of collision and visual objects
Collision Objects
  Geometry that defines a colliding surface
Joints
Visual Objects
  Geometry that defines visual representation
  Constraints between links
Sensors
  Collect, process, and output data
Plugins
  Code attached to a World, Model, Sensor, or the simulator itself

## Slide 8: Element Hierarchy

## Slide 9: World
A world is composed of a model hierarchy
The Gazebo server (gzserver) reads the world file to generate and populate a world
This file is formatted using SDF (Simulation Description format) or URDF (Unified Robot Description Format)
Has a “.world” extension
Contains all the elements in a simulation, including robots, lights, sensors, and static objects
Willow Garage World

## Slide 10: Models
Each model contains a few key properties:
  Physical presence (optional):
    Body: sphere, box, composite shapes
    Kinematics: joints, velocities
    Dynamics: mass, friction, forces
    Appearance: color, texture
  Interface (optional):
    Control and feedback interface (libgazebo)

## Slide 11: Element Types
Collision and Visual Geometries
  Simple shapes: sphere, cylinder, box, plane
  Complex shapes: heightmaps, meshes

## Slide 12: Element Types
Collision and Visual Geometries
  Simple shapes: sphere, cylinder, box, plane
  Complex shapes: heightmaps, meshes
Joints
  Prismatic: 1 DOF translational
  Revolute: 1 DOF rotational
  Revolute2: Two revolute joints in series
  Ball: 3 DOF rotational
  Universal: 2 DOF rotational
  Screw: 1 DOF translational, 1 DOF rotational

## Slide 13: Element Types
Sensors
  Ray: produces range data
  Camera (2D and 3D): produces image and/or depth data
  Contact: produces collision data
  RFID: detects RFID tags
Lights
  Point: omni-directional light source, a light bulb
  Spot: directional cone light, a spot light
  Directional: parallel directional light, sun
LiDAR sensor in Gazebo

## Slide 14: How to use Gazebo to simulate your robot?
Steps:
load a world
load the description of the robot
spawn the robot in the world
publish joints states
publish robot states
run rviz

## Slide 15: Libraries/Tools available with ROS
Image Courtesy: Open Source Robotics Foundation