## Slide 1: Introduction to ROS SERVICE

## Slide 2: SERVICES
In ROS (Robot Operating System), services allow nodes to send a request and receive a response.
ROS services work as a client server interaction model.
Where the server offers a specific service and clients can request that service.
A node can implement one or more services.
Any node can call a service.(client)
Calls are synchronous .

## Slide 4: Steps
Create ROS package
Create ‘srv’ directory and ‘srv file’
    roscd ros_service
    mkdir srv
catkin_create_pkg ros_service rospy
cd ..
catkin_make
source devel/setup.bash

## Slide 5
In the srv directory create a file called ServiceExample.srv and write the below three lines:
    int32 a
    int32 b
    ---
    int sum
    The three dashes mark the end of the input(s) and the beginning of the output(s).

## Slide 6: Update package.xml
Open the package.xml file and write the below lines. If you put the rospy dependency when you create the ROS package, you should already have into the file the rospy build depend and run depend. Otherwise, put all the below lines into the package.xml:
    <build_depend> rospy</build_depend> <exec_depend> rospy</exec_depend> <build_depend> message_generation</build_depend> <exec_depend> message_runtime</exec_depend>

## Slide 7: Update CMakeLists.txt
find_package(catkin REQUIRED COMPONENTS
  roscpp
  rospy
  message_generation
  )
add_service_files(
  FILES
  ServiceExample.srv
  )
generate_messages(
  DEPENDENCIES
  std_msgs
  )

## Slide 8
Run the catkin_make command to generate the classes used to interact with the service.
  catkin_make
  source devel/setup.bash
Write callService.py
In the srv directory create a new file called callService.py.
Make this file executable using the command “chmod +x callService.py”.
The file shows a simple server that accept as input one or zero and as output it returns ON or OFF

## Slide 9: Server.py
#!/usr/bin/env python3 import rospy from ros_service.srv import TwoInts, TwoIntsResponse def handle_add_two_ints(req): return TwoIntsResponse(req.a + req.b) def add_two_ints_server(): rospy.init_node('add_server') s = rospy.Service('add_two_ints', TwoInts, handle_add_two_ints) rospy.loginfo("Ready to add two ints.") rospy.spin() if __name__ == "__main__": add_two_ints_server()

## Slide 10: Client.py
#!/usr/bin/env python3 import rospy from ros_service.srv import TwoInts def add_two_ints_client(x, y): rospy.wait_for_service('add_two_ints') try: add_two_ints = rospy.ServiceProxy('add_two_ints', TwoInts) resp1 = add_two_ints(x, y) return resp1.sum except rospy.ServiceException as e: print("Service call failed: %s" % e) if __name__ == "__main__": rospy.init_node('add_client') x = 5 y = 3 print("Requesting %d + %d" % (x, y)) print("Sum: %d" % add_two_ints_client(x, y))